## Slide 1
MARCH 17, 2025
VLA_Digital_Twin
Amaan Siddiqui
Weekly Progress -2nd Jan, 2026

## Slide 2
Current Weeks Progress
  Successfully integrated lerobot/smolvla_base model from hugging face with a “hybrid PID+VLA” architecture to test pick and place implemented last week using the manual PID controller.
  Integrated 3 camera feeds (main 640×480, front, gripper chase) with consistent resolution for VLA input, real-time dashboard rendering, and live cube tracking.
  To solve latency issues tried developing a non-blocking VLA inference using Python threading to prevent 100-200ms inference time but still working on it.
  Currently, VLA inference is taking around 2000ms on Apple Silicon MPS (expected: 100-150ms), causing 18+ second sync offset and preventing successful grasp.

## Slide 3
  Migrate to lab GPU workstation, targeting 80-120ms inference time and sync offset reduction from 2,000ms to <50ms for real-time control.
  Experimenting on either migrating to complete VLA controller or to continue with the hybrid controller approach based on better synchronization results.
  Try to tune other parameters by experimentation (like the steps after which the vla inference must be called to generate the results, better prompt for VLA etc) to reduce the latency and sync_offset.
Next Weeks Goals